## Slide 1: Online health status detection of a motor
Gianluca Salata, 25/08/2021
MAS513-Advanced Robotics project:
PROBLEM: Is it possible to determine the health status of the motor continuously using non-contact sensors and non-destructive testing?

## Slide 2: State of art:
Gianluca Salata, 25/08/2021
Detection of the health status of the motor using contact sensor such as:
Temperature sensor
Vibrometer/accelerometer
Voltmeter and ammeters.
Estim.
useful
life
defects
bearings
Temperature
The vibration of the shaft is related to defects of the inner components of the motor, i.e. bearings. Each harmonics is associated to a specific fault.

## Slide 3: Project’s aim
Gianluca Salata, 25/08/2021
LIDAR
GOOD
BAD
The aim is to determine the continous health status of the motor using a non-contact sensors that measure the vibration of the shaft.
PROS:
Non intrusive monitoring system
Mostly independet from enviroment condition
Retrace the fault
CONS:
Exspensive
More complex
PC

## Slide 4: Process
Gianluca Salata, 25/08/2021
CWFM Lidar generates a voltage signal
Fourier trasformaton of the signal to obtain the range o the shaft
Plotting istantenous range with time we obtain the displacement
Analysing harmonics of the displacement to detect known fault
PC

## Slide 5: Future applications and developments
Gianluca Salata, 25/08/2021
Condition monitoring without contact with the object can be very useful when the motor is placed in hostile or not very accesable enviroment.
The data from the sensing components can be used for the control system of the motor, improving efficiency.
The health of the motor can helps to develop new predictive maintenance technique, reducing the costs of industrial installations.